HW status
Our recent developments:
Switching Core
Routing Table Unit
Network Interface Controller
Endpoint extensions
V3 tech spec

---
HW status
What we worked on (blue)

---
Switching core (swcore)
Generic multiport packet queue (not Ethernet-specific)
Store-and-Forward architecture
Non-blocking (full gigabit upstream/downstream on each port)
WRF inteface I/O
Programmable number of priority levels
Can support different memories for packet storage

---
Switching core
N configurable WRF inputs/outputs
N routing control inputs associated with WRF inputs
Unicast, multicast and broadcast
Flow control on each port

---
Switching core – block diagram

---
Routing Table Unit (RTU)
Programmable number of ports
Implements programmable packet matching engine
802.1q support
Priority evaluation (per-port, per-MAC, per-VLAN)

---
Routing Table Unit (RTU)

---
Network Interface Controller (NIC)
PTP-enabled Network Card
Connected to “virtual” 11th port of the switch core
Compatible with Linux driver model
Linux sees it as a 10 separate network interfaces
corresponding to physical ports in the switch
Possibility of DMA operation

---
Network Interface Controller (NIC)

---
Endpoint extensions
Detachable PCS (Physical Coding Sublayer) with IEEE - standardized register set
Initial support for Virtex/Spartan GTP serdes
Flow control support
802.3z autonegotiation support
More flexible buffering
WRF-based I/O

---
Endpoint extensions