White Rabbit in Action:
distributed synchronization concepts and demo
Adam Wujek, Dimitris Lampridis
1st White Rabbit Tutorial Workshop
7 October 2017
Barcelona, Spain

---
The White Rabbit project
A solution to problems in distributed
real-time controls and data acquisition
Based on well-known technologies
Open Hardware and Open Software
with commercial support
International collaboration
Many users: CERN, GSI, KM3NET, cosmic ray detectors, metrology labs...

---
The White Rabbit project
White Rabbit is an extension of Ethernet
Standard Ethernet network
Ethernet features (VLAN)
& protocols (SNMP)
High accuracy synchronization
Reliable and low-latency Control Data

---
The content of a White Rabbit kit
GM
Switches
Nodes
Fibers
SFPs
Monitoring (optional)
BC1
BC2
Node
Node
Node
Node
Node
Node

---
The content of a White Rabbit kit
GM
SFPs
Fibers
Switches
Nodes
Monitoring (optional)
BC1
BC2
Node
Node
Node
Node
Node
Node

---
Small form-factor pluggable transceiver (SFP)
Converts electrical signal into a laser light
… and vice versa
Very simple design
Single fiber
Single mode
RX and TX use different wavelength
(e.g. 1310nm and 1490nm)
Up to 10km transmission*
*for recommended SFPs; with different SFPs hundreds of km possible
http://www.axcen.com.tw
[Speaker Notes: http://www.axcen.com.tw/app_script/DisplayCut.ashx?rootDir=upload/pro_kind/&File=201703291414570.jpg&W=398&H=357]

---
The content of a White Rabbit kit
GM
SFPs
Fibers
Switches
Nodes
Monitoring (optional)
BC1
BC2
Node
Node
Node
Node
Node
Node

---
Fiber
Single mode
Compatible with ITU G.652
LC connectors
http://www.cablestogo.com
http://www.fs.com

---
Precision Time Protocol (IEEE 1588)
Frame-based synchronisation protocol.
Simple calculations:
Link delayms
Clock offsetms = t2 − t1 + δms
Disadvantages:
Assumes symmetry of medium
All nodes have free-running oscillators
Frequency drift compensation vs. message exchange traffic
size 20 { color navy {δ_{ms}={(t_{4}−t_{1})-(t_{3}−t_{2})} over {2}}}

---
WR Link model
Static hardware delays: ∆TXM, ∆RXM , ∆TXS, ∆RXS
Semi-static hardware delays: εM, εS
Fiber asymmetry coefficient:
size 20 { color navy {%alpha={δ_{MS}−δ_{SM}} over {δ_{SM}}}}
Calibration procedure to find ∆TXM, ∆RXM, ∆TXS, ∆RXS and α.
WR Master
WR Slave
WR gear
WR gear

---
Dispersion
https://pl.wikipedia.org/wiki/Plik:Prisms_with_high_and_low_dispersion.png

---
Is the correction needed?
Link ~5km
~400ps RTT difference between day and night
>1ns due to the weather

---
The content of a White Rabbit kit
GM
SFPs
Fibers
Switches
Nodes
Monitoring (optional)
BC1
BC2
Node
Node
Node
Node
Node
Node

---
White Rabbit Switch (WRS)
Central element of WR network
18 port gigabit Ethernet switch with WR features
One management port (separated from WR network)
Fully open design, commercially available

---
White Rabbit Switch
Simplified block diagram of the hardware

---
White Rabbit Switch
Simplified block diagram of the hardware

---
White Rabbit Switch
Simplified block diagram of the hardware

---
White Rabbit Switch
Simplified block diagram of the hardware

---
White Rabbit Switch
ARM CPU:
Management of a switch
Web interface
SNMP
WR PTP daemon (PPSi)
Handles WRS firmware upgrade
Configures FPGA at boot
Updates routing table

---
WRS: Configuration file
Contains:
Management interface’s configuration
Ports’ configuration (calibration values, mode)
Remote log server address
Log verbosity level
VLANs configuration
and more

---
WRS: Configuration file
Kconfig format
The same as used by Linux Kernel
{key}={value} format
CONFIG_ETH0_DHCP=y
# CONFIG_ETH0_DHCP_ONCE is not set
# CONFIG_ETH0_STATIC is not set
CONFIG_HOSTNAME_DHCP=y
# CONFIG_HOSTNAME_STATIC is not set
[...]
CONFIG_REMOTE_SYSLOG_SERVER="be-co-tracing"
CONFIG_REMOTE_SYSLOG_UDP=y
CONFIG_WRS_LOG_HAL="daemon.info"
CONFIG_WRS_LOG_LEVEL_HAL="0"
[...]
#
# Port Timing Configuration
#
CONFIG_PORT01_PARAMS="name=wri1,proto=raw,tx=223897,rx=226273,role=master,fiber=0"
CONFIG_PORT02_PARAMS="name=wri2,proto=raw,tx=224037,rx=226377,role=master,fiber=0"
CONFIG_PORT03_PARAMS="name=wri3,proto=raw,tx=224142,rx=226638,role=master,fiber=0"
CONFIG_PORT04_PARAMS="name=wri4,proto=raw,tx=224313,rx=226471,role=master,fiber=0"

---
WRS: Config file handling
Local on a switch
Retrieved from a network at boot (via TFTP, FTP or HTTP)
Path to a config provided in a DHCP response
WR Switch
Server
Time
DHCP request
DHCP response with config location
Config file TFTP request
TFTP transfer with config

---
WRS: Editing config file
In text editor
CONFIG_ETH0_DHCP=y
# CONFIG_ETH0_DHCP_ONCE is not set
# CONFIG_ETH0_STATIC is not set
CONFIG_HOSTNAME_DHCP=y
# CONFIG_HOSTNAME_STATIC is not set
[...]
CONFIG_REMOTE_SYSLOG_SERVER="be-co-tracing"
CONFIG_REMOTE_SYSLOG_UDP=y
CONFIG_WRS_LOG_HAL="daemon.info"
CONFIG_WRS_LOG_LEVEL_HAL="0"
[...]
#
# Port Timing Configuration
#
CONFIG_PORT01_PARAMS="name=wri1,proto=raw,tx=223897,rx=226273,role=master,fiber=0"
CONFIG_PORT02_PARAMS="name=wri2,proto=raw,tx=224037,rx=226377,role=master,fiber=0"
CONFIG_PORT03_PARAMS="name=wri3,proto=raw,tx=224142,rx=226638,role=master,fiber=0"
CONFIG_PORT04_PARAMS="name=wri4,proto=raw,tx=224313,rx=226471,role=master,fiber=0"

---
WRS: Editing config file
In text editor
Kconfig tools (make menuconfig, make nconfig etc.)

---
WRS: Editing config file
In text editor
Kconfig tools (make menuconfig, make nconfig etc.)
Web interface

---
WRS: Editing config file
In text editor
Kconfig tools (make menuconfig, make nconfig etc.)
Web interface
Controls Configuration Data Editor (CCDE)

---
Switch Demo

---
Demo setup
Oscilloscope
GM
PPS
CH1
CH2
CH3
CH4
Fibers
Copper Eth.

---
Demo setup
Oscilloscope
GM
PPS
CH1
CH2
CH3
CH4
PPS
BC1
Fibers
Copper Eth.

---
Demo setup
Oscilloscope
GM
5km
PPS
CH1
CH2
CH3
CH4
PPS
BC1
Fibers
Copper Eth.

---
The content of a White Rabbit kit
GM
SFPs
Fibers
Switches
Nodes
Monitoring (optional)
Fibers
BC1
Copper Eth.
BC2
Node
Node
Node
Node
Node
Node

---
White Rabbit Nodes
VME64x and PCIe carriers with FPGA and FMC slots
Other, community provided carriers (PXIe, cRIO, etc.)
WR PTP core in FPGA disciplines local clocks and provides timecode interface (TAI and PPS).

---
White Rabbit PTP Core (WRPC)
Portable, well documented, System-on-Chip design
Provides a control interface, a timing interface and a bidirectional data streaming interface
Detailed presentation later today

---
WRPC Hardware Requirements
A supported FPGA family
One SFP, two voltage-controlled oscillators and accompanying DACs, all wired to the FPGA

---
Node Demo

---
Demo setup
Oscilloscope
GM
5km
PPS
CH1
CH2
CH3
CH4
PPS
PPS
BC1
Fibers
Coaxial
Node
Copper Eth.
PC1

---
Hot Air-Gun Demo

---
WR hot-air gun demo: test setup
PPS
GM
5km
PPS
PPS
BC2
Fibers
Coaxial
Node
Copper Eth.
Oscilloscope
CH1
CH2
CH3
CH4