Softcores – CPUs in the FPGA
Wesley W. Terpstra
from BEL
http://bel.gsi.de

---
What is a Softcore?
A full CPU
Implemented in HDL
Synthesized and loaded into an FPGA
Connected to the FPGA bus

---
Why use a Softcore? (vs. HDL)
Re-use large body of C/java/etc code
Easier to reason about, debug, and trace
A single component to solve many tasks
Even more reconfigurable than an FPGA

---
Why use a Softcore? (vs. CPU)
Direct access to on-chip bus
Same clock domain (WB)
Nothing between devices and code
(Deterministic, Low latency, Simple)
Customizable instructions
One less part
(but way way way slower)

---
Two routes for an Operating System
Full operating system (Linux) or bare metal (library OS)?
+ More compatible software
+ Re-use of device drivers
- Lose direct access to SoC bus
- Requires a lot of memory (2MB+ vs. 4kB)
- More complex / things to break
If you need full OS, you probably want a real CPU

---
Softcore Political Requirements
Open Source
Portable (Altera, Xilinx, Lattice, ... future proof)
Tweakable (custom instructons, bus choice, ...)
Well documented, tested, and supported
Eliminates almost all open source softcores
Survivors: LM32, LEON3, OpenRISC, (ZPU)

---
Softcore Technical Requirements
Requirement	Purpose	Issues
Gcc-toolchain	re-use of C	-
JTAG access	debug bus, load F/W	ZPU
Debug support	trace program	ZPU, (LM32)
Small	OR, LEON3
Fast	ZPU
Best choice: LM32 if it had a portable debugger

---
Size/speed trade-offs (Ballpark)
CPU	Mhz	Size (LEs)
ZPU	300	400
LM32	250	900
LEON3	175	2500
OpenRISC	150	3700
(All numbers are for an Altera Arria2)

---
Size/speed trade-offs (Ballpark)
CPU	Mhz	Size (LEs)	Cycles/mul
ZPU	300 175	400	576+
LM32	250 175	900	1
LEON3	175	2500	1
OpenRISC	150	3700	1
(All numbers are for an Altera Arria2)

---
PHASE: gdb/LM32 on Altera/Xilinix/..
FTDI
ByteBlaster
JTAG
BitBanger
JTAG
Chain
GDB
GDB RSP
LM32
DROM
LM32
JTAG
Altera
SldHub

---
LM32 Processor Overview
32-bit RISC architecture
32 registers
8-16 control registers
no side-effects / flags
5-stage pipeline
single cycle issue
1-3 cycle result
Harvard architecture

---
LM32 Processor Options
Feature	Size	Impact Suggestion
Instruction cache	++	++++	KEEP
Data cache	+++	+	-
Multiplier	.	+	KEEP
Barrel shifter	.	+	KEEP
Divider	+++	+	-
JTAG access	++	DEBUG
Watch/breakpoints	+	DEBUG
32 Interrupts	+	++	KEEP

---
Questions?