Etherbone – Wishbone on IP
Wesley W. Terpstra
from BEL
http://bel.gsi.de

---
What is Wishbone?
Wishbone: a System-on-Chip (SoC) bus
Connects devices inside an FPGA
Very simple interface due to common clock domain
Version B.4 supports pipelined streams

---
Remote Wishbone?
Would be nice to access the bus outside FPGA
Debugging
Bulk firmware loading
Direct control/reset of embedded devices
For the FAIR project: control of the timing system

---
Etherbone = Remote Wishbone
Etherbone packs Wishbone bus cycles on top of UDP
Ethernet
IPv4
UDP
Etherbone
Cycle #1
Cycle #2

---
Etherbone Goals
 For Etherbone to be useful in FAIR it must have:
Reliable delivery
Deterministic delay
Gigabit throughput
Low latency
Building on a standard like UDP/IP is nice:
Routable over more than just Ethernet
Interoperable with existing operating systems

---
Reliability vs. Determinism
Unfortunately, the usual approach to network reliability,
retransmission, breaks deterministic delivery times!
Solution:
Forward-Error-Correction (FEC) at Ethernet layer

---
The need for speed
Gigabit is fast.
Packets must include significant payload.
Streaming is fast.
We aim to make Etherbone streaming
This has two tough repercussions:
Header fields cannot depend on payload
Wishbone devices have a response deadline

---
Header Fields with Dependencies
IP packet length
IP checksum
UDP length
UDP checksum
Ethernet
IPv4
UDP
Etherbone
Cycle #1
Cycle #2

---
Header Dependencies: Length
IP packet length
UDP length
If responses have the same length
as requests, we can stream replies.
Ethernet
IPv4
UDP
Etherbone
Cycle #1
Cycle #2

---
Header Dependencies: Checksums
Only covers IP header, which is mostly constant.
Add a few variable fields in and done.
IP checksum
UDP checksum
Can use 0 to mean not provided
Ethernet
IPv4
UDP
Etherbone
Cycle #1
Cycle #2

---
Etherbone Format: Transform in Place

---
Status of Implementation
Two implementations:
VHDL: Wishbone MAC <=> WB master
C89 library: UDP/IP from OS or raw FEC ethernet
C library has bindings for: C++, Pascal, Python(?)
GUI for control of C library (as DLL)

---
Etherbone Software Library
C/C++
Manual
UDP/IP
FEC library
Raw Eth
socket
EB
library
Pascal
UDP socket
Python?
TCP socket

---
Etherbone Software Library
Linux
C/C++
Manual
UDP/IP
FEC library
Raw Eth
socket
EB
library
WINDOWS
Pascal
UDP socket
Python?
TCP socket

---
Future Directions
In my opinion, Etherbone is missing two things
TCP/IP transport
Reliability outside WhiteRabbit
For latency problem
Wishbone bus scanning
Etherbone talks to random FPGAs
Would be nice to detect what it is!

---
Questions?